## Slide 1: Lab 5 SoC design and optimization
CE 435
Embedded Systems
Dimitris Christodoulou 2113
Theologis anthimopoulos 2195

## Slide 2: SOBEL FILTER
CONTENT
SOBEL in Software Optimization
SOBEL in Hardware Optimization

## Slide 3: SOBEL FILTER
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
Gx
Gy
BEFORE
AFTER

## Slide 4: SOFTWARE results
SOLUTION | TIME | PSNR
SOLUTION 1 | 1.704671 | inf
SOLUTION 2 | 0.087745 | inf
SOLUTION 3 | 0.066042 | inf
SOLUTION 4 | 0.045589 | 28.6625

## Slide 5: SOLUTION 1
Run Sobel Filter Code without any optimizations.

## Slide 6: SOLUTION 2
Decreased running time using optimization level: Optimize most (-O3).

## Slide 7: SOLUTION 3
Changed the order of double for loop so as to calculate pixels row-by-row instead of column-by-column.

## Slide 8: SOLUTION 4
Finally, replaced Euclidean distance with Manhattan distance in order to decrease the run time.

## Slide 9: Inf PSNR VS 28.6624 PSNR

## Slide 10
Chart: STATISTICS
| SOLUTION 1 | SOLUTION 2 | SOLUTION 3 | SOLUTION 4
Series 1 | 1.7046 | 0.087745 | 0.066042 | 0.045589
Chart: 
| SOLUTION 2 | SOLUTION 3 | SOLUTION 4
Series 1 | 0.087745 | 0.066042 | 0.045589

## Slide 11: HARDWARE OPTIMIZATION
SOLUTIONS | TIME | PSNR
SOLUTION 1 | 2,095958 | inf
SOLUTION 2 | 1,276471 | inf
SOLUTION 3 | 0,980560 | 28.6625
SOLUTION 4 | 0,508779 | 28.6625
SOLUTION 5 | 0,027544 | 28.6625
SOLUTION 6 | 0,023087 | 28.6625
SOLUTION 7 | 0,012605 | 28.6625

## Slide 12: Solution 1
Run Sobel Filter Code without any optimizations.
Used m_axi for input and output.
Another pragma will be added with this with the port name “return”.

## Slide 13: Solution 1

## Slide 14: Solution 2
Added another directive to convolution2D external for-loop. (Pipeline II = 1)
Replaced multiplications with shift registers.
Changed the order of double for loop so as to calculate the row-by-row pixels

## Slide 15: Solution 3
After that, replaced Euclidean distance with Manhattan distance so as to decrease the running time.
Removed convolution2D for-loop.

## Slide 16: Solution 4
Added two sobel filters to Block Design.
Divided the picture and sent each half to each sobel filter.

## Slide 17: Solution 4

## Slide 18: Solution 5
Added another directive to sobel internal for-loop (Pipeline). Used memcpy to load 3 rows at first and another one for each row.
Added four sobel filter to Block Design. Calculate four segment simultaneously.

## Slide 19: Solution 5

## Slide 20: Solution 6
Changed the clock period to vivado hls. Decreased clock from 10ns to 8ns. Also, increased frequency from 100 MHz to 125Mhz.

## Slide 21: Solution 7
Changed the requested frequency. Increased frequency from 125MHz to 250MHz.

## Slide 22
Utilization Estimates
Latency
(clock cycles)

## Slide 23
Chart: STATISTICS
| SOLUTION 1 | SOLUTION 2 | SOLUTION 3 | SOLUTION 4 | SOLUTION 5 | SOLUTION 6 | SOLUTION 7
Series 1 | 2.096 | 1.2765 | 0.98056 | 0.50878 | 0.027544 | 0.023087 | 0.012605
Chart: 
| SOLUTION 5 | SOLUTION 6 | SOLUTION 7
Series 1 | 0.027544 | 0.023087 | 0.012605

## Slide 24: SUMMARY
SOFTWARE
HARDWARE
FIRST TIME : 1,704671
LAST TIME : 0,045589
165,9
FIRST TIME : 2,095958
LAST TIME : 0,012605
208,4
97.33%
99.4%

## Slide 25: SOFTWARE VS HARDWARE
BEST SOFTWARE TIME : 0,045589
BEST HARDWARE TIME : 0,012605
3,5
Chart: 
| SOFTWARE | HARDWARE
Series 1 | 0.045589 | 0.012605
72.4%

## Slide 26
Thank you for your attention!
Questions and comments are welcome!